## Slide 1: Deprecating ASM for Interdomain Multicast draft-acg-mboned-deprecate-interdomain-asm-00
Mikael Abrahamsson, mikael.abrahamsson@t-systems.de
Tim Chown, tim.chown@jisc.ac.uk
Lenny Giuliano, lenny@juniper.net
(and probably Toerless  )
IETF 101, London, 20 Mar 2018

## Slide 2: Draft history
Original purpose:
  Document multicast service models (at a high level)
  Discuss their use cases; document deployment examples
  And, importantly, to recommend use of SSM
Feedback given at IETF 99 and IETF 100:
  Strip back on text on the models
  Focus on deprecating interdomain ASM and promoting use of SSM
  Don’t preclude use of intradomain ASM
Result: draft-acg-mboned-deprecate-interdomain-asm-00 posted, which aims to define more specifically what we mean by deprecating interdomain ASM

## Slide 3: Reminder of one of the drivers for this work…
Initial proposal made by David Farmer on Internet2 multicast list
  See https://lists.internet2.edu/sympa/arc/wg-multicast/2017-06/msg00001.html
“I propose that general purpose classic IPv4 ASM be deprecated on the Internet2 R&E Backbone. The primary propose of this change is to simplify multicast support for the new MPLS based R&E Backbone, by mostly eliminating the need for MSDP. SSM for both IPv4 and IPv6, and Embedded-RP for IPv6, should continue to be supported on the Internet2 R&E Backbone, as they do not require MSDP. ”

## Slide 4: Draft structure
Intro
Brief ASM / SSM description
Discussion of ASM and SSM deployment
Advantages of SSM for interdomain multicast
Recommendations
  Primarily deprecating ASM for interdomain
  … plus related topics
Note on congestion control
Security considerations

## Slide 5: High-level statement
“This document recommends the deprecation of the use of Any-Source Multicast (ASM) for interdomain multicast.
It recommends the use of Source-Specific Multicast (SSM) for interdomain multicast applications, and that hosts and routers that are expected to handle such applications fully support SSM.
The recommendations in this document do not preclude the continued use of ASM within a single organisation or domain, and are especially easy to adopt when already using the preferred ASM protocol options there (PIM-SM).”

## Slide 6: 4.1: Deprecating ASM for interdomain
Deprecate ASM for interdomain multicast
Implicitly all hosts and routers supporting such applications fully support SSM
  BCP for interdomain SSM is in RFC 8313
Applies to MSDP (IPv4) and Embedded-RP (IPv6)
Recommends against use of PIM-SM with an RP where multicast tunnels are used between domains
Interdomain means “run on routers operated by two or more separate operational entities”
More inclusive interpretation includes devices under different operator control, e.g., set-top boxes
Not making MSDP Historic (allows for intradomain use)

## Slide 7: 4.2: Network support for IGMPv3/MLDv2
Recommends all hosts supporting multicast and any security appliances handling it support IGMPv3 and MLDv2
(See also RFC 4604)
RFC6434-bis makes MLDv2 a MUST in hosts
Snooping MUST support IGMPv3 and MLDv2
(See also RFC 4541)

## Slide 8: 4.3/4.4: Building application support for SSM
Applications should use SSM, and operate correctly in an SSM environment, triggering IGMPv3/MLDv2 messages to signal use of SSM
Added note on programming language support
  Noted current websockets limitation
If feasible, we recommend making applications use SSM, even if initially for use in an intradomain environment supporting ASM
  Noting the operational simplifications also apply intradomain
  And that PIM-SSM is a subset of PIM-SM
Implicitly pushing source discovery above network layer

## Slide 9: 4.5/4.6: Further work for IETF?
Documenting common practices for SSM support in applications
  Converting ASM applications into SSM ones
  Best practice for SSM support in greenfield designs
Documenting an ASM/SSM protocol mapping mechanism
  a mechanism to translate a (*,G) join or leave to a (S,G) join or leave, for a specific source, S
  Some vendor–specific mechanisms exist today; a standardised one would be desirable?
  Would be an interim solution (yeah, but….)

## Slide 10: 4.7: Filtering ASM ?
While ASM is deprecated interdomain, we recommend NOT filtering such addresses, to allow for development and deployment of the mapping mechanism
May recommend this in the future

## Slide 11: 4.8: Not precluding intradomain ASM
Intradomain ASM is still common today in enterprises and campuses
“This document does not preclude continued use of ASM in the intradomain scenario. If an organisation, or AS, wishes to use multiple multicast domains within its own network border, that is a choice for that organisation to make, and it may then use MSDP or Embedded-RP internally within its own network.”

## Slide 12: Thoughts?
Are we now heading in the right direction?
What do we do with the text we cut from the previous draft-acg-mboned-multicast-models-02 document?
  Park it until this document is done?
We made suggestions in the new draft to work on
  BCP to convert ASM applications into SSM application
  Documenting an ASM/SSM protocol mapping mechanism
Comments?